Filtering
Digital Filtering
- Convolution of time series
- Convolution as filtering process
- Cross- and auto-correlation
- Frequency filtering
- Deconvolution
Reading:
  - Telford et al., Sections A.10,11

---
Convolution  of time series
Convolution
of time series
- Convolution for time (or space) series is what commonly is multiplication for numbers.
- Example of a ‘convolutional model’:	rise in lake level resulting from rainfall
  - Let’s assume that the recorded rainfall over 5 months is: 2, 3, 1, 4, 3 cm, respectively.
  - The lake level will respond to a 1 cm of rain fall, say, with a 2-cm rise in the first month and 1-cm in the second. This is called the ‘impulse response’.
  - Lake level rises from the different months of rainfall will accumulate linearly.

---
Lake level rise Numerical example
Lake Level Rise
Numerical example
The resulting lake levels can be calculated by the following procedure, called convolution:
The impulse response series is reversed and shifted, and sample-by sample dot product is taken to find the response at any moment

---
Convolution General formulae
Convolution
General formulae
The resulting lake levels can be calculated by the following procedure, called convolution. Convolution of two series, ui, and wi, denoted u*w, is:
As multiplication, it is symmetric (commutative):
Note that if we need to multiply two polynomials, with coefficients uk and wk, we would use exactly the formula above. Therefore, in Z or frequency domains, convolution becomes simple multiplication of polynomials (show this!):
This is the key property facilitating efficient digital filtering.

---
Convolution Two important cases of interest
Convolution
Two important cases of interest
Digital signal filtering
Earth’s response is also a filter. Note that in this case, the impulse response is unknown and is of primary interest
Hence reflection processing deals with inverse filtering… (i.e., finding the filter)

---
Convolutional model of a reflection seismic trace
Convolutional model
of a reflection seismic record
Reflection seismic trace is a convolution of the source wavelet with the Earth's ‘reflectivity series’

---
Convolutional model 2
Convolutional model
A more realistic example
From Yilmaz, 1987

---
Cross- and Auto-correlation
Cross- and Auto-correlation
Cross-correlation gives the degree of similarity between two signals:
  - For each value of a ‘lag’ i:
  - Shift the second trace by the lag
  - Calculate dot product:
The lag for which the cross-correlation is largest gives the time shift between the two records
A most important application – pre-processing of Vibroseis recordings
Auto-correlation of a record is its cross-correlation with itself
It is symmetric in terms of positive and negative lags
It indicates the degree to which the signal repeats itself.

---
Frequency Filtering
Linear Filtering
Most operations with seismic signals can be represented by a convolutional operator:
    - It is linear:
    - It is translationally (time-) invariant:
  - The filtering operator is represented differently in different domains:
    - Convolution in time domain
    - Complex-value multiplication in Z- and frequency domains
      - This allows easy frequency filtering (selective enhancement or suppression of harmonic components in the signal)
v=F u
F (u_1+u_2) = F u_1 + F u_2
F {time shifted}_t(u) = {time shifted}_t(F u)

---
Frequency Filtering
- Key element of seismic and GPR processing.
- Low-pass (high-cut), Band-pass, High-pass (low-cut), Notch
  - Suppressing the unwanted (noisy) parts of the frequency spectrum.
  - Usually zero-phase, to avoid phase (travel-time) distortion. This means that the filter does not change the phase spectrum.

---
Filter panels
Filter panels
Trial band-pass filter panels are designed in order to determine the best frequency range for data display and analysis. For a final display, time-variant filters are used.

---
Deconvolution
Deconvolution
Deconvolution (inverse) filters
  - To remove (reduce) the effects of wavelet’s complexity on the resulting image.
  - Based on the known (or estimated) wavelet shape, an inverse filter is designed with the objective to compress this wavelet in time:
Numerous deconvolution techniques are available
Performed in time or frequency domains.

---
Deconvolution example (shot gathers)
Deconvolution
(shot gathers)
From Yilmaz, 1987

---
Deconvolution example (stack)
Deconvolution
(stack)
Interpreters certainly prefer working with the crisper, high-resolution image (b) that uses deconvolution.
From Yilmaz, 1987

---
S/N enhancement
Example of
Multichannel filter:
Stacking
Records are summed ('stacked') in order to increase the S/N ratio:
  - Signal is assumed the same in all channels, therefore, its amplitude is increased N (the number of records);
  - For incoherent noise, the energy becomes proportional to N, and so the amplitude increases as ;
  - Therefore, the S/N ratio  .
  - Note: coherent noise cannot be suppressed by stacking!
sqrt{N}
sqrt{N}
From Reynolds, 1997