GEOL 335 (2018/19-02) Homework assignment #4

Instructor:  Prof. I. Morozov		  	         Due: Apr 5 2019

- [20%] Illustrate the phenomenon of frequency folding mathematically. To do this, consider sampling rate of fs samples per second and give the expression for the Nyquist frequency fN. Follow this procedure:

  - Write an expression for a harmonic (sine or cosine) function of time at frequency fN+f.

  - Consider the values of this function at sampling times, that is, at tk = kt (how is t related to fs and fN?).

  - Show that the harmonic function taken at sampled times only is equivalent to another one with frequency fN – f.

- [20%] Seismic reflections are recorded by receivers planted on the sea floor. The ghost reflection from the sea surface acts as a “notch” filter, i.e., filter removing certain frequency from the reflected waves. Derive a formula for this frequency as a function of water depth h and ray parameter p. Remember that the reflection from the surface is of negative polarity.

- [20%] Consider two finite time series u = {2,5,-2,1} and v = {6,-1,-1}.

  - Convolve these two series. Do not forget about negative lags.

  - Cross-correlate the same two series. For what lag are these time series most similar?

- [20%] Show that the autocorrelation u(k) of time series {uk}, taken at lag samples k = i – j can be given by:

- [20%] The dominant period of marine seismic sources is often determined by the source depth. In this case, the second (negative) half-cycle of the downgoing wave is reinforced by the ghost reflection from the surface. Assuming that this is true for the source signatures shown below, determine their depths. Take VW = 1500 m/s for the acoustic wave velocity in water.

The sources shown here are: a) single 120 cubic inch airgun (B1, B2, and B3 are bubble oscillations); b) array of airguns of different sizes selected to attenuate bubble effects; c) sleeve exploder.