## Slide 1
Receiver and source coordinates
Source station ‘1002’ is a spurious one I created by mistake.
We used inline numbers 101-105

## Slide 2
Trial 200-Hz sine function signal at shot point 1
Note the variations of amplitudes (bottom plot)

## Slide 3
Shot point 1 on the left – general view

## Slide 4
Zoom in of the same with first-arrival picks
Measure (rough) pulse width and frequencies of the swings you can see in the data
Channel 5 is perhaps the easiest

## Slide 5
Strong zoom for measuring velocity
Draw a straight line approximating ALL 8 points and measure slope

## Slide 6
Different source (that eroded hook) at the same source point. Are the records much different?

## Slide 7
Source point 4 (on the side)
For a bonus, can you estimate wave velocity from this shape or travel-time curve (hyperbola)?

## Slide 8
Strike on the right.
Measure the velocity again and compare to the one from the left

## Slide 9
Vibrator signal near channel 1 ( 100 to 5000 Hz sweep in 1 sec)
Note that the strongest signal is near channels 2-5 (plot on the bottom)

## Slide 10
Zoom-in into the same sweep records

## Slide 11
Spectra of the sweep signals (lower-left plot)
Have we really achieved 5 kHz frequencies on this table?
What frequencies are there?

## Slide 12
Sweep records after cross-correlating each channel with channel 1. This creates (imperfect here) pulses which I picked by ‘x’
Measure wave velocity using these ‘x’. Is it close to the one you had before?

## Slide 13
Starting location tests
Here is the map of actual locations
(all coordinates are multiples of 0.3 m)

## Slide 14
Location of strike #1 using travel times (crosses ‘x’) in the upper-right plot)
The inverted location is shown by green ‘x’ here
Color shows a sum of travel-time misfits (the smallest value is white, where the final location is)
This plot shows measured wave-onset times (black ‘x’) and modelled times (red)
They look quite close?
This plot shows travel times vs. source-receiver distance. Slope of this red line gives velocity within the floor
Summary of results:
Black circles are possible source locations FROM THE VIEWPOINTS of the individual stations.
The correct location is where all these circles intersect

## Slide 15
This is a test inverting not observed but MODELED travel times from source #1.
The location is PERFECT – all black circles intersect at the correct point, and all travel times are predicted accurately (red line on the upper-right)

## Slide 16
Another pretty good location, but maybe a little off (green cross).
Which source was it?
What is the location error?
Compare velocity values.

## Slide 17
Another location, OUTSIDE of the area covered by receivers
Same questions as in the preceding slide?