GEOL 483.3 (2017/18-02) Homework assignment #2

Instructor:  Prof. I. Morozov				 		       Due: Feb 15 2018

- Substitute solution  (that is: , where and  are the scalar and vector potential functions, respectively) into the equation of motion discussed in class:

(note the summation in repeated subscripts).

- [15%] Show that this equation reduces to two independent equations containing only or  These equations correspond to P- and S-waves, respectively.

- [10%] Show that a gradient of any field can be added to , without changing the values of U.

- [15%] A harmonic wave is travelling through the Earth with velocity 4 km/s. Assuming that the maximum strain equals 10-8, what is the maximum particle displacement for waves with frequencies: a) 1 Hz, b) 10 Hz, c) 100 Hz?

- [10%] Is it possible to have spherical symmetry for an S-wave propagating away from a point source? Explain. From this, can you suggest how a point, pure explosive source (which is spherically-symmetric) can generate S waves?

- [25%] An elastic body is uniformly stretched in all directions: x ( (1+)x , y ( (1+)y, z ( (1+)z. Express:

- Strain tensor,

- Dilatational strain, 

- Stress tensor

- Deviatoric strain is defined as , where  is the dilatational strain, , and constant a is selected so that the trace of equals zero: . Thus, deviatoric strain describes the variation of the shape of the body without changing its volume.

  - [10%] Derive the value of a.

  - [15%] Express the elastic-energy density within an elastic body:

in terms of the dilatational and deviatoric strains.